## Slide 1
C:\Users\dtdb7\AppData\Roaming\QGIS\QGIS3\profiles\default\processing\models
PASTE THE STREAM GENERATION MODULE IN FOLLWING PATH OF YOUR SYSTEM:

## Slide 2
OPEN THE DEM FILE(.BIL FORMAT) IN GLOBAL MAPPER AND CHANGE THE PROJECTION AS UTM AND EXPORT REQD AREA IN .TIFF FORMAT

## Slide 3
TAKE THE UTM DEM AND LCC SEED .DGN FILE IN YOUR FOULDER

## Slide 4
OPEN THE UTM DEM IN SURVEYKSHAK
TYPE STR IN PROCESSING MENU

## Slide 5
OPEN THE STREAM GENERATION MODULE

## Slide 6
SELECT THE UTM DEM & RUN

## Slide 7
AUTO PROCESS WILL START AND WILL BE COMPLETED IN 5 TO 10 MIN

## Slide 8
STREAM AND CONTOUR WILL BE GENERATED

## Slide 9
CONTOUR AND STREAM WILL BE GENERATED. GO TO PROJECT AND EXPORT TO .DXF FORMAT

## Slide 10
OPEN THE .DXF CONTOUR FILE IN MICROSTATION V8 AND EXPORT IT TO 2D .DGN FILE

## Slide 11
OPEN THE 2D FILE IN V8 AND EXPORT TO V7

## Slide 12
OPEN THE V7 FILE IN MGE CHECK THE HEIGHT VALUES AND CONVERT IT TO LCC/WGS 84